## Slide 1
Presidency
School of Engineering
1
Presidency

## Slide 2
Department of
Electronics and Communication Engineering

## Slide 3
Basics of Electronics and Communication Engineering (ECE3107)
L-T-P-C: 3-0-0-3
By
Dr. K. Gowri
Assistant Professor – Senior Scale
Department of Electronics and Communication Engineering
Presidency University, Bengaluru

## Slide 4
MODULE 2
Vision algorithms and applications:
Transforming sensor reading, Mapping Sonar Data, aligning laser scan measurements - Vision and Tracking: Following the road, Iconic image processing, Multiscale image processing
Video Tracking - Learning landmarks: Landmark spatiograms, K-means Clustering, EM Clustering.

## Slide 5
2.1 Transforming sensor reading
Introduction:
The presence of sensors in the ubiquitous environment has led to the production of an enormous amount of data.
These sensors belong to diverse categories including planar pressure, thermal, optical, acoustic, and proximity modalities.
They provide information for activity recognition and context-aware models that could be used for a wide range of applications such as automatic monitoring in the smart environment and wellness scene, computer-human-interaction, user experience, etc.

## Slide 6
2.1 Transforming sensor reading
There has been extensive research on wearable and pervasive sensors, which record and sense data in the context of human activities; ranging from physical activities (running, sleeping, walking, etc.), such as monitoring gym exercises, analyzing gait patterns, to biological activities (breathing, eating, etc.), such as breathing detection, eating and drinking arm gesture detection.
The task of extracting useful information from the raw sensor data has been performed using various machine learning and data mining techniques.

## Slide 7
2.1 Transforming sensor reading
Usually, when the raw sensor data is concerned, the feature extraction is done using statistical methods involving the calculation of the mean, standard deviation, maximum and minimum values.
These features have proven to be quite reliable in tasks related to classification, recognition and segmentation.
Deep learning, Convolutional neural networks (CNN), Recurrent neural networks (RNN) – popular in achieving superhuman accuracy on image classification tasks.

## Slide 8
2.1 Transforming sensor reading
Both, CNN and RNN have been used in combination to create systems which are capable of understanding images, and to provide temporal context to these individual images.
Limitations: requirement of large amounts of labeled data to facilitate the training of these very deep networks.
While the computer vision community has facilitated this requirement with large labeled datasets, such as, the ImageNet and MS-COCO datasets for object recognition, classification, detection and captioning; for various other tasks not many labeled datasets exist.

## Slide 9
2.1 Transforming sensor reading
The above-mentioned limitation can be bypassed by performing transfer learning, i.e., using labeled data from one domain and transferring the learned knowledge to a target domain.
Transfer learning involves using the knowledge acquired on a specific task, and adapting this knowledge to a different, but related task.
A common scenario for transfer learning involves using a convolutional neural network trained on a very large dataset, and then fine-tuning it on the target dataset which is relatively small in size.

## Slide 10
2.1 Transforming sensor reading
A domain is said to be easily visually interpretable if by looking at its visual representation, a human can extract relevant information and sense of the meaning it conveys.
For example, images of everyday objects such as automobiles, animals, landscapes; documents, X-ray, and MRI scan data all belong to the category of easily visually interpretable images.
An average human can easily learn to distinguish between different classes, e.g., several sub-species of animals, or several models of automobiles.
Doctors or radiologists analyze and interpret MRI or X-ray data to detect irregularities in healthy organs.

## Slide 11
2.1 Transforming sensor reading
The application of transfer learning on such images is feasible for mainly two reasons.
It is possible due to their nature of being visually meaningful.
There are large datasets from the same domain available within the community to carry out the transfer learning tasks.
However, there exists types of data, such as sensor data, which are not easily visually interpretable, and it is unclear if it would be possible to visually interpret them.
Not visually interpretable data can be, for example, position updates of moving objects in location-based services, fluctuations in the stock market, medical experimental observations, or streaming sensor data.

## Slide 12
2.1 Transforming sensor reading
Sensors:
Over the past decades, the availability of sensors has increased substantially and enabled makers and designers to prototype interactive objects rapidly and at low cost.
However, this large variety of components also comes with the challenge of selecting the right sensor from many similar components to find the one that best fits the use case at hand.
Since each sensor has its own specification, understanding what each sensor can sense and how it will work on a prototype can be a time-consuming process.

## Slide 13
2.1 Transforming sensor reading
Limitations of reading sensor data:
Extracting information from a datasheet can be cumbersome and confusing since the sensing information may be buried among the chip design, schematic, and other technical aspects.
Datasheets are not standardized, which makes comparing sensors with each other a difficult task.
Since datasheets are text documents, it can be hard to picture what sensors can sense when placed on a prototype.

## Slide 14
2.1 Transforming sensor reading
Different Stages of Prototyping with Sensors
Sensor Specifications from Datasheet
Sensor Data Overlay over the Physical Prototype via AR
Live and Recorded Sensor Data Visualization

## Slide 15
2.1 Transforming sensor reading
Library of visualization primitives:
Dimensionality:
We represent discrete data as a point and continuous data as a bar.
We represent directional data as bars in different directions.
For volumetric data, we display the data as a 3D volumetric shape (e.g., a cone or hemisphere). Dimensional information is rendered as a black outline with no infill.

## Slide 16
2.1 Transforming sensor reading
Range
To visualize the range of a sensor, we use the min/max values from the datasheet as the bounds of the visualization.
For continuous non-spatial and directional data, we define the lower bound of the visualization to be equal to the minimum value and the upper bound of the visualization to be equal to the maximum value specified in the datasheet.
For spatial data, the visualization shows the lower and upper bounds of the sensing volume in the size as specified in the datasheet.

## Slide 17
2.1 Transforming sensor reading
Resolution:
We visualize resolution by splitting the bar or volume into segments, with smaller segments representing higher sensor resolutions than larger segments.
We compute the segment size by dividing the sensor’s output bit resolution by the range of the sensor.

## Slide 18
2.1 Transforming sensor reading
Sensor Values
We visualize live sensor values by filling in the point, bar, or volume.
For discrete values, if a ’zero’ is read, the point is rendered in 0% opacity and if a ’one’ is read, it is rendered in 100% opacity.
Makers can differentiate between a ’zero’ reading and ’no data’ using the text label that shows the current value.
For continuous values, the larger the received sensor values, the more of the bar or the volume is rendered in 100% opacity.

## Slide 19
2.1 Transforming sensor reading
Textual information
We use labels to display the range (min/max), the resolution, and the current sensor value.
For directional data, we also label the axes information, and for volumetric data, we label the angle of the feld of view.
Makers can choose in the user interface which information they want to display.

## Slide 20
2.1 Transforming sensor reading

## Slide 21
2.1 Transforming sensor reading
Additional Visualizations Attributes:

## Slide 22
2.1 Transforming sensor reading

## Slide 23
2.1 Transforming sensor reading
Steps to transform sensor reading:
Loading Sensor Information from Sensor Database
Visualizing Sensor Data
Augmented Reality visualization
Reading Live Sensor Values
Recording Sensing Data
Sensing Area Overlap

## Slide 24
2.2 Mapping SONAR Data
Advances in technology have since enabled the deployment of Remotely Operated Vehicles (ROVs) and Autonomous Underwater Vehicles (AUVs), which have revolutionized ocean exploration by automating complex tasks and reducing dependence on human operators.
Despite these technological advancements, underwater navigation and object detection remain challenging due to the limitations of optical sensors.
Water turbidity, light attenuation, and scattering severely degrade visual data quality, making camera-based imaging unreliable in most sub-sea operations.

## Slide 25
2.2 Mapping SONAR Data
Sonar technology has emerged as a viable solution for underwater detection and navigation, as it operates using acoustic waves that can penetrate murky waters and function independently at ambient lighting conditions.
Sonar systems are generally categorized into single-beam and multi-beam types.
Multi-beam sonars provide extensive spatial coverage and high-resolution 3D reconstructions, but their cost and complexity limit accessibility for smaller research or commercial platforms.

## Slide 26
2.2 Mapping SONAR Data
Sonar technology has emerged as a viable solution for underwater detection and navigation, as it operates using acoustic waves that can penetrate murky waters and function independently at ambient lighting conditions.
Sonar systems are generally categorized into single-beam and multi-beam types.
Multi-beam sonars provide extensive spatial coverage and high-resolution 3D reconstructions, but their cost and complexity limit accessibility for smaller research or commercial platforms.

## Slide 27
2.2 Mapping SONAR Data
Single-beam sonars—such as the Blue Robotics Ping360—employ a mechanically rotating transducer to sweep across a specified range, generating 2D polar representations of the surrounding environment.
The sonar scanned the environment incrementally, recording intensity values within a range of 0-255 at each angular position.
These intensity values represent the strength of acoustic reflections from objects within the field of view.
The raw Ping360 sonar output is inherently represented in polar coordinates (range versus bearing).

## Slide 28
2.2 Mapping SONAR Data
Each beam corresponds to a specific bearing angle, and each range bin encodes the reflected amplitude.
For interpretability and machine learning analysis, these polar data are converted into Cartesian occupancy maps, where both axes rep- resent spatial distance.
Signal filtering is used to ensure only valid data points within the useful scanning range were retained for analysis.
Following this, a statistical threshold approach was applied to further refine the region of interest (ROI) .
This approach ensured the removal of noise while preserving significant reflections from objects.

## Slide 29
2.2 Mapping SONAR Data
The data is manually inspected and transformed into polar coordinates and converted into a grayscale image format for training the deep learning networks.
With this types of input, the model learns to separate objects from the back- ground based on intensity variations detected by the sonar.

## Slide 30
2.3 Aligning LASER Scan Measurements
Precise localization is a prerequisite for many autonomous systems, such as robotics, unmanned aerial vehicles, etc.
Also, indoor positioning is an especially challenging problem, where localization cannot be achieved by GPS due to the satellite signal being greatly attenuated.
While the traditional radio-based indoor positioning technologies, such as Bluetooth, Wi-Fi, Radio-frequency Identification (RFID) and ultra-wideband (UWB), still have some disadvantages in terms of low accuracy, high latency, electromagnetic interference or high hardware cost.

## Slide 31
2.3 Aligning LASER Scan Measurements
The localization technology based on visible light communication (VLC), which is referred as visible light positioning (VLP), has attracted intensive attention as it can provide high accuracy positioning based on the existing lighting infrastructure.
The modulated LED broadcasts its unique identity (ID) via switching at a high frequency imperceptible to the human eye, but which can be recognized by photodiodes (PD) and rolling shutter effect (RSE) cameras.
The LED-ID can be mapped/modulated once for all since they are normally fixed and not easily vulnerable to environmental changes.

## Slide 32
2.3 Aligning LASER Scan Measurements
Sensors are imperfect, and their measurements are prone to errors.
Sensors should be carefully mounted and aligned in order for your application to receive optimum results.
Navigation denotes the robot’s ability to determine its own position in its frame of reference and then to plan a path towards some goal location.
The most important consideration to reduce measurement error is aligning the sensor beam so that it is parallel to the dimension to be measured.

## Slide 33
2.3 Aligning LASER Scan Measurements
The easiest example to describe is height.
If we want to measure the height of an object with a ruler, you would want that ruler to be perfectly up and down.
If the ruler weren’t perfectly up and down, we’d expect an error with your measurement.
It’s the same with the laser beam on our sensors.
We’d ideally want to align the beam so that it is perfectly up and down to measure height.
Any deviation from that alignment would introduce an error in the measurement.

## Slide 34
2.3 Aligning LASER Scan Measurements
While truly perfect alignment is impossible, with care and a well-made fixture or alignment bracket, we often can get the alignment accurate enough to reduce the alignment error to significantly less than the sensor’s error.
The angle between the beam and the surface of the target can also be a source of error.

## Slide 35
2.3 Aligning LASER Scan Measurements
The reasons for the laser beam of the sensor is to strike the target surface as close to perpendicular as possible.
While the laser spot from our sensors often looks like a single point on the target, it does have a diameter.
# The more angled the target is, the more the spot stretches out on the target.
#This does make it more difficult for the sensor to know where the center of that spot is, and that can cause errors.

## Slide 36
2.3 Aligning LASER Scan Measurements
An angled target will usually reflect more light away from the sensor’s detector.
# The less light the detector gets, the harder it is for the sensor to distinguish the measurement from other light noise.
# That can reduce the measurement accuracy, increase the measurement time, or both.
# This problem increases with the shininess of the target.

## Slide 37
2.3 Aligning LASER Scan Measurements
3. An angled or rough target that is shiny can cause the opposite problem — direct reflection into the detector.
# If there is “specular” or direct reflection, that shows up on the detector as a second peak that has no relation to the distance.
# This can result in measurements that are completely incorrect or keep the sensor from offering a measurement at all.

## Slide 38
2.3 Aligning LASER Scan Measurements

## Slide 39
2.3 Aligning LASER Scan Measurements
3D laser scanner measurement:
It is an advanced method for precise three-dimensional measurement of objects using laser line triangulation sensors, also known as laser scanners.
This technology enables the accurate determination and comparison of measured values such as length, width, height, angle, radius, flatness, parallelism, diameter, defect sizes and more.
Unlike traditional 2D image processing with cameras, 3D laser scanner measurement enables a three-dimensional representation of an object.

## Slide 40
2.3 Aligning LASER Scan Measurements
3D laser measurement of an aluminium block

## Slide 41
2.3 Aligning LASER Scan Measurements
Typical industries and sectors where 3D laser scanner measurement is used include:
Metalworking
Mechanical Engineering
Welding technology
Automotive
Battery manufacturing
Aerospace
Smartphone manufacture

## Slide 42
2.3 Aligning LASER Scan Measurements
3D laser measurement

## Slide 43
2.4 Vision and Tracking
The sense of vision is a powerful and dominating sense in humans.
A typical approach is to use a video camera as a visual sensor.
The subjective experience of understanding the content of a visual scene is often as simple as opening one’s eyes — there seems to be little or no conscious effort involved in perceiving a three-dimensional world filled with objects and surfaces both near and far.

## Slide 44
2.4 Vision and Tracking
The perception is so effortless that it is possible, even typical, to underestimate the difficulty of duplicating the feat with a video camera.
The lack of effort also belies the amount of neural hardware that goes into this visual illusion.
Extracting information from a video sequence is a computationally intensive and difficult problem.
While the field of computer vision continues to make important advances, it would be premature to consider it a problem solved.

## Slide 45
2.4 Vision and Tracking
Fig. 2.4.1 Pin-hole camera (a) and its mathematical model (b).

## Slide 46
2.4 Vision and Tracking
Issues that make computer vision difficult.
1. Information is lost in the 3D to 2D transformation.
A pin-hole camera is a closed container with a small hole on one side.
Light rays enter through the hole, illuminating the back wall with the color of the object from which they were reflected and thereby painting an image on the wall.
The image is upside-side down and reversed because of the path the light rays travel.
This relationship between the object and its image is often modeled mathematically as a perspective projection (shown in fig 2.4.1).

## Slide 47
2.4 Vision and Tracking
The image plane in (fig 2.4.1 (b)) is shown with a coordinate system aligned and centered on the camera axis.
The image plane is located a distance f from the origin, which is the optical center of the camera.
Let the coordinates of a point on the image plane be .
Since the image plane is positioned at distance f from the center of projection, the three dimensional coordinates of that point are
Following a line from the origin through [u, v, f]T and out to the object, call the coordinates of the point that the ray intersects on the object

## Slide 48
2.4 Vision and Tracking
The relationship of the image coordinates and object coordinates can be written:
Thus, information is lost in the 3D to 2D transformation.
This is the first problem that makes computer vision difficult: the 2D structure seen on the image is related in a complex way to the 3D structure of the original scene.

## Slide 49
2.4 Vision and Tracking
2. To a computer, the image has to be understood pixel by pixel and clearly separable into regions.
An image is represented on a computer as an array of pixels.
Each pixel corresponds to the intensity and the color of light integrated over a small area of the image.
A pixel can be represented as a single value, corresponding to the total intensity of light in that area.
It can also be represented as a n-tuple of values in some color space.
A typical color space is RGB (Red-Green-Blue).

## Slide 50
2.4 Vision and Tracking
A large variety of colors can be represented by a linear combination of the ‘standard’ red, green and blue primary colors- the coefficients in this linear combination are the pixel’s RGB values.
These will often be numbers between 0 and 1.
For example: the RGB value (1, 0, 0) would denote a pixel that is 100% red; (0.25, 0.25, 0) would be a pixel with 25% red and 25% green, a dark yellow; (0, 0, 0) would be black; and (1, 1, 1) would be white.

## Slide 51
2.4 Vision and Tracking
Figure 2.4.2 illustrates a second difficulty in computer vision.
To a human, a scene such as Figure 2.4.2(b) consists of some objects —mountains, trees, river — positioned in the scene relative to each other.
To a computer, the image has to be understood pixel by pixel, as in Figure 2.4.2(a) and the scene viewed at this scale is far less clearly separable into regions corresponding to objects.

## Slide 52
2.4 Vision and Tracking
Fig 2.4.2 (a) Close up (b) of a section of a digital image.

## Slide 53
2.4.1 Vision and Tracking: Following the road
Consider the problem illustrated in Figure 2.4.3
This figure shows a robot using its visual sensor to navigate along a path delineated by white lines on the ground.
The problems involved are to first identify the lanes (the white lines in the image) and then determine where these lines are in space with respect to the robot.
We will look at some of the computational steps in road following and how this might be done on a cluster.
A robot such as the Pioneer 3-AT shown in Figure 2.4.3(a) does not typically carry an onboard cluster.

## Slide 54
2.4.1 Vision and Tracking: Following the road
Figure 2.4.3: (a) Robot lane following (b) lane closeup and (c) thresholded Cb component of closeup.

## Slide 55
2.4.1 Vision and Tracking: Following the road
However, it is not unreasonable to expect that such machines will carry multiprocessor, multicore computers in the near future.
More sophisticated robots, such as Junior, the Stanford University entry in the DARPA Urban Challenge already carry multiprocessor, multicore systems onboard.

## Slide 56
2.4.1 Vision and Tracking: Iconic image processing
Always we need to preprocess the image at the pixel level.
The noise introduced into the image by the camera or random lighting effects may need to be reduced.
Aspects of the image such as edges or regions of color may need to be enhanced.
These operations consider the image only to be a collection of pixels, and operate pixel by pixel, (or pixel by small regions of pixels).
This kind of processing is called image processing to distinguish it from operations the iconic at attempt to identify 3D structure, objects or shapes in the image.

## Slide 57
2.4.1 Vision and Tracking: Iconic image processing
Iconic image processing is typically more suited to fine grain, massively parallel, single instruction multiple data architectures.
However, as long as the image information can be moved efficiently enough, cluster processing of images can also be effective.
One approach to avoiding image transfer costs is to equip individual nodes in the cluster with separate cameras.
Examples of pixel-based iconic image operation include color space transformations, color filtering, intensity transformations and so forth.

## Slide 58
2.4.1 Vision and Tracking: Iconic image processing
For example, the difference between the white lines and the grass background in Fig. 2.4.3 (a) becomes much more apparent when the color space is changed from RGB to the luma-chroma colors space YCrCb.
Subsequently restricted to just the Cb chroma component, and finally thresholded to a binary image.
Thresholding is also a pixel-based iconic image processing operation.
Pixels in the thresholded binary image are set to 1 if the pixels in the original image have a value greater than the threshold value and are set to 0 otherwise.

## Slide 59
2.4.1 Vision and Tracking: Iconic image processing
Changes in the lighting of a natural scene are typically not very noticeable to a human observer, but can cause a great deal of difficulty in analysis of images.
A scene might have overall increases or decreases in light intensity due to the time of day or weather conditions.
There may also be shadow effects as lighting sources move due to the time of day, or as objects move in or adjacent to the scene.
Another reason to use YCrCb, rather than RGB, for the analysis of natural images (such as Figure 2.4.3(a)) is that the CrCb chroma (or color) components are less sensitive to changes in light intensity.

## Slide 60
2.4.1 Vision and Tracking: Iconic image processing
The scene lighting intensity variations are mostly confined to the Y luma component.
In RGB all three components can vary with intensity.
Hence, the Cb component is a more reliable ‘white line’ detector over a wide range of lighting conditions.
The formulae to change RGB to YCrCb (from the CCIR-601 digital video standard) are:

## Slide 61
2.4.1 Vision and Tracking: Iconic image processing
Notice that there are quite a few isolated white speckles in the image in Figure 2.4.3(c).
These could be reduced by reducing the threshold value.
However, if we do that, we may also reduce the amount of the white line that is visible.

## Slide 62
2.4.1 Vision and Tracking: Iconic image processing
Analysis:
Let the time taken to color convert and threshold 1 pixel be χ.
In that case, the serial time to process an n×m image is easily calculated as Ts = nmχ.
The parallel communication time is composed of the time to scatter the color image strips and to gather the thresholded image back again.
The time to scatter the image strips from the root to each processor is given by λlog p + 3nm(p − 1)/pβ.

## Slide 63
2.4.1 Vision and Tracking: Iconic image processing
The time to gather the result image back to the
root is λlog p + nm(p − 1)/pβ.
The parallel calculation time is nmχ/p.
Figure 2.4.4: Performance graph for parallel pixel-based operations for 640 × 480 image (λ = 3μs, β = 1Gbps, χ = 730 ns).

## Slide 64
2.4.1 Vision and Tracking: Iconic image processing
The total parallel time is therefore,

## Slide 65
2.4.1 Vision and Tracking: Spatial pixel operations
There is an important class of pixel-based operations that involves looking at pixels in a small region of the image.
One such operation, for example, calculates the value of a pixel by averaging the values of the eight pixels that surround that pixel.
When this is applied to each pixel in an image the result is a blurring or smoothing effect on the image.
Figure 2.4.5(a) shows the lane close-up view from Figure 2.4.5.
Figure 2.4.5(b) shows the results of a blurring operation performed on the lane close-up image.

## Slide 66
2.4.1 Vision and Tracking: Spatial pixel operations
Figure 7-5: (a) Original image; (b) smoothed; (c) edges.

## Slide 67
2.4.1 Vision and Tracking: Spatial pixel operations
Another useful spatial operation is one that sharpens the image (e.g., Figure 2.4.5(c)).
In this case, the central pixel of the neighborhood, is the sum of the differences between the central pixel’s original value and the value each of its eight neighbor pixels.
A convenient way to express spatial operations of this sort is as a convolution operation.
The convolution operation makes use of a convolution kernel G, a q × r matrix.
Typically q = r, and r n, r m, where n ×m are dimensions of the image I.

## Slide 68
2.4.1 Vision and Tracking: Spatial pixel operations
No matter what the kernel contains, the convolution H is always defined for each point (x, y) in the image I as:
Fig. 2.4.6 shows a sharpening kernel and a portion of an image.
The kernel is applied to each pixel in succession starting at the top left and working to the bottom right.

## Slide 69
2.4.1 Vision and Tracking: Spatial pixel operations
Figure 7-6: 3 × 3 Image convolution example.

## Slide 70
2.4.1 Vision and Tracking: Spatial pixel operations
The pixel value at (x, y) is replaced by the sum of the product of the (i, j) element of the kernel with the (x + i −r/2, y + j − 1/2) pixel of the image for all i and j.

## Slide 71
2.4.1 Vision and Tracking: Multiscale image processing
There is an advantage to inspecting an image at several scales, because the objects in an image can vary in apparent size due to visual perspective.
It is useful to combine the results of applying pixel-based image operations at several different image scales.
Consider the three images shown in Figure 2.4.8.
These show the result of processing the scene in Figure 2.4.3(a) with a pixel-based edge operation, an operation that identifies the intensity changes that typically occur at the edges of objects or color regions in an image and which can also be done using convolution.

## Slide 72
2.4.1 Vision and Tracking: Multiscale image processing
Figure 7-8: Multiscale edge operations on the scene in Figure 7-3(a).

## Slide 73
2.4.1 Vision and Tracking: Multiscale image processing
The identified edges show up as white pixels in these images.
The operation was performed with the same kernel size on the original sized image (the leftmost image in Figure 2.4.8), then on an image with half the height and width dimensions of the original (the second image on the left), and so forth, from left to right.
The result images have all been resized identically in Figure 2.4.8 for ease of comparison.

## Slide 74
2.4.1 Vision and Tracking: Multiscale image processing
The result images have all been resized identically in Figure 7-8 for ease of comparison.
The image on the left shows the most detailed breakdown of edges: details of the wheels of the robot are visible as is texture along the white lane lines.
The image on the right the least detail: the robot is visible mainly as a rectangular region and the white line lines are devoid of internal detail.

## Slide 75
2.4.1 Vision and Tracking: Multiscale image processing
A number of multiscale processing operations have been developed.
SIFT features (Scale Invariant Image Transform features) use a multiscale measurement to identify image features that are unique across a range of scales, image rotations and translations.

## Slide 76
2.4.1 Vision and Tracking: Multiscale image processing
Partitioning
The serial implementation of a multiscale image operation would proceed by processing each scaled image in turn.
Let there be s scales.
The full sized image will be n rows by m columns.
Each successive image will be half the row size and half the column size of the next larger image.
If the time to process the full size image is nmχ, then the next smaller scaled image will take nmχ/4 and the next smaller will be nmχ/16 and so forth.

## Slide 77
2.4.1 Vision and Tracking: Multiscale image processing
This is a geometric progression with ratio 1/4. The total time taken to process s scales will therefore be,

## Slide 78
2.4.1 Vision and Tracking: Multiscale image processing
Where ξ(s) is the sum to s terms of the geometric progression.
If we partition this processing on the cluster with row stripes as we did before, we have a parallel calculation time of since each processor just does the processing for every scale on its row strip of the image in parallel.
The communication time for this approach is the same as for the previous single-scale, pixel-based operations.

## Slide 79
2.4.1 Vision and Tracking: Multiscale image processing
Each partition will process its scale in parallel, so the calculation time in this case is the time for the largest scale (taking the longest time) to finish:
This is the same as for the simpler row stripe partition, so there is no calculation advantage in partitioning by scale.

## Slide 80
2.4.1 Vision and Tracking: Multiscale image processing
a